## Slide 1: RECTIFIED TRIANGULAR WAVE
GROUP 10:
Aswini Samantray (12140360)
Sujeet Kumar (12141610)
EE 204 Analog Circuits Project
Instructor: Dr. Rinkee Chopra

## Slide 2
LTSpice Model

## Slide 3: Components:
Component | Quantity
LM324 IC | 1
Jumper Wires | -
1uF capacitor | 1
1N4007 diode | 1
10K ohm Resistance | 2
8.2K ohm resistance | 2
1.2K ohm Resistance | 2

## Slide 4
LM324 Pin configuration

## Slide 5: Working of Triangular Waveform generator
At U3,
V+ = V01(R3/R1+R3) + V0(R1/R1+R3)
Case 1: V+ > V- :
V01 = VSAT
Case 2 : V+<V- :
V01 = -VSAT
At U1
Due to virtual short, V- = 0
I = V01/R2, Ic = Cdvc/dt ➡∫dvc=(1/c)(∫Icdt)
V0 = -Vc ➡ V0= - (1/c)(∫(V01/R2)dt

## Slide 6: Working of Half Wave Rectifier
For Vi>0,
Diode D1 will be ON and diode D2 will be OFF,
Hence, due to virtual short, V0= 0V,
For Vi<0,
Diode D1 will be OFF and D2 will be ON,
Due to virtual short,
V0 = -Vi(R5/R4)

## Slide 7: Parameters Calculation
The peak to peak output of Triangular wave is : - Vp-p = 2(R3/R1)(VSAT)
Let Vp-p= 5V ➡ 5=2(1K/R1)(10V) ➡ R1 = 4K
The frequency of V0 is given by :- f = R1/(4R3R2C)
Here, C = 1uF ➡ R2 = 1K (at f = 1kHz)
For Half Wave Rectifier.
R4 = R5= 10K

## Slide 8: Output Waveforms

## Slide 9: THANK YOU